## Slide 1: Multi-Commodity Flow Based Routing
Set up ILP formulation for MCF routing
  Capacity of each edge in G is 2
  Each edge in G becomes a pair of bi-directional arcs in F
  n1 = {a,l}, n2 = {i,c}, n3 = {d,f}, n4 = {k,d}, n5 = {g,h}, n6 = {b,k}

## Slide 2: Flow Network
Each arc has a cost based on its length
  Let xek denote a binary variable for arc e w.r.t. net k
  xek = 1 means net k uses arc e in its route
  Total number of x-variables: 16 × 2 × 6 = 192

## Slide 3: ILP Objective Function
Minimize

## Slide 4: ILP Demand Constraint
Utilize demand constant
  zvk = 1 means node v is the source of net k (= −1 if sink)
  Total number of z-constants: 12 × 6 = 72

## Slide 5: ILP Demand Constraint (cont)
Node a: source of net n1

## Slide 6: ILP Demand Constraint (cont)
Node b: source of net n6

## Slide 7: ILP Capacity Constraint
Each edge in the routing graph allows 2 nets

## Slide 8: ILP Solutions
Min-cost: 108 (= sum of WL), 22 non-zero variable

## Slide 9: ILP-based MCF Routing Solution
Net 6 is non-optimal
  Due to congestion

## Slide 10: Drawback of ILP-based Method
ILP is non-scalable
  Runtime quickly increases with bigger problem instances
Shragowitz and Keel presented a heuristic instead
  Called MM (MiniMax) heuristic [1987]
  Repeatedly perform shortest path computation and rip-up-and-reroute

## Slide 11: MM Heuristic
Initial set up: shortest path computation
  Ignore capacity, some paths are not unique

## Slide 12: First Iteration of MM Heuristic
Step 1
  Capacity of channel c(e,f) and c(d,i) is violated
  Max overflow M1 = 3 − 2 = 1 > 0, so we proceed
  Notation: channel c(e,f) represents arc pair (e,f) and (f,e)

## Slide 13: First Iteration of MM Heuristic (cont)
Step 2
  Set of channels with overflow of M1: J1 = {c(d,i), c(e,f)}
  Set of channels with overflow of M1 and M1 − 1 : J10 = {c(a,d), c(e,h), c(i,j), c(j,k), c(d,i), c(e,f)}
Step 3
  Cost of J10 = {c(a,d), c(e,h), c(i,j), c(j,k), c(d,i), c(e,f)} is ∞

## Slide 14: First Iteration of MM Heuristic (cont)
Step 4
  Set of nets using channels in J1: K1 = {n1, n2, n3, n4, n5, n6}
  Set of nets using channels in J10: K10 = K1

## Slide 15: First Iteration of MM Heuristic (cont)
Step 5
  Compute shortest paths for nets in K1 using new cost (= Step 3)
  n1 & n6 have non-infinity cost, so we proceed

## Slide 16: First Iteration of MM Heuristic (cont)
Step 6
  Net with minimum wirelength increase between n1 & n6: k0 = n1

## Slide 17: First Iteration of MM Heuristic (cont)
Step 7
  Use new routing for n1
  Wirelength didn’t change, but congestion improved

## Slide 18: Second Iteration of MM Heuristic
Details in the book
  Use new routing for n3
  Wirelength increased (due to detour in n3), but congestion improved