## Slide 1: Yoshimura-Kuh Channel Routing
Perform YK channel routing with K = 100
  TOP = [1,1,4,2,3,4,3,6,5,8,5,9]
  BOT = [2,3,2,0,5,6,4,7,6,9,8,7]

## Slide 2: Constrained Left-Edge Algorithm
First perform CLE on original problem (for comparison)
  Assign VCG nodes with no incoming edge first
  Use tracks top-to-bottom, left-to-right

## Slide 3
Zone Representation
Horizontal span of the nets and their zones
  TOP = [1,1,4,2,3,4,3,6,5,8,5,9]
  BOT = [2,3,2,0,5,6,4,7,6,9,8,7]

## Slide 4: Net Merging: Zone 1 and 2
We compute
  L = {1} and R = {4}
  Net 1 and 4 are on the same path in VCG: no merging possible

## Slide 5: Net Merging: Zone 2 and 3
We compute
  L = {1,2} and R = {5,6} (= net 1 inherited from last step)
  Merge-able pairs: (2,5) and (2,6) (= not on the same path in VCG)

## Slide 6: Net Merging: Zone 2 and 3 (cont)
Choose the “best” pair between (2,5) and (2,6)
  We form P = {5,6} and Q = {2} and choose best from each set
  We compute
    u(2) = 4, d(2) = 1, u(5) = 3, d(5) = 4, u(6) = 4, d(6) = 2
  Only 1 element in Q, so m* = net 2 trivially

## Slide 7: Net Merging: Zone 2 and 3 (cont)
Now choose “best” from P
  We compute g(5,2) and g(6,2) using K = 100
  Since g(5,2) > g(6,2), we choose n* = net 6
  We merge m* = 2 and n* = 6
    Likely to minimize the increase in the longest path length in VCG

## Slide 8: Net Merging: Zone 2 and 3 (cont)
Merged net 2 and 6
  We had P = {5,6} and Q = {2}, and need to remove 2 and 6
    Q is empty, so we are done with zone 2 and 3
  We had L = {1,2} and R = {5,6}, and need to remove 2 and 6
    We keep L = {1}
  Updated zone representation and VCG

## Slide 9: Net Merging: Zone 3 and 4
We compute
  L = {1,3,4} and R = {7} (= net 1 inherited from last step)
  All nets in L and R are on the same path in VCG
    no merging possible

## Slide 10: Net Merging: Zone 4 and 5
We compute
  L = {1,3,4,26} and R = {8,9}
  Merge-able pairs: (4,8), (4,9), (26,8), (26,9)

## Slide 11: Net Merging: Zone 4 and 5 (cont)
Choose m* from Q
  We form P = {4,26} and Q = {8,9}
  We compute
    u(4) = 3, d(4) = 3, u(26) = 4, d(26) = 2, u(8) = 4, d(8) = 3, u(9) = 5, d(9) = 2

## Slide 12: Net Merging: Zone 4 and 5 (cont)
Choose m* from Q (cont)
  We find m* from Q that maximizes
    f(8) = 100 · {u(8) + d(8)} + max{u(8), d(8)} = 704
    f(9) = 100 · {u(9) + d(9)} + max{u(9), d(9)} = 705
  So, m* = 9

## Slide 13: Net Merging: Zone 4 and 5 (cont)
Choose n* from P
  We compute g(4,9) and g(26,9) using K = 100
  Since g(4,9) > g(26,9), we get n* = net 26
  We merge m* = 9 and n* = 26

## Slide 14: Net Merging: Zone 4 and 5 (cont)
Merged net 26 and 9
  We had P = {4,26} and Q = {8,9}, and need to remove 26 and 9
    Q is not empty, so we repeat the whole process
  Updated P = {4} and Q = {8}
    Trivial to see that m* = 8 and n* = 4, so we merge 8 and 4
  Updated zone representation and VCG

## Slide 15: Routing with Merged Nets
Perform CLE on merged netlist
  Use tracks top-to-bottom, left-to-right

## Slide 16: Comparison
Net merging helped
  Reduce channel height by 1