## Slide 1: Mincut Placement
Perform quadrature mincut onto 4 × 4 grid
  Start with vertical cut first
undirected graph model w/ k-clique weighting
thin edges = weight 0.5, thick edges = weight 1

## Slide 2: Cut 1 and 2
First cut has min-cutsize of 3 (not unique)
  Both cuts 1 and 2 divide the entire chip

## Slide 3: Cut 3 and 4
Each cut minimizes cutsize
  Helps reduce overall wirelength

## Slide 4: Cut 5 and 6
16 partitions generated by 6 cuts
  HPBB wirelength = 27

## Slide 5: Recursive Bisection
Start with vertical cut
  Perform terminal propagation with middle third window

## Slide 6: Cut 3: Terminal Propagation
Two terminals are propagated and are “pulling” nodes
  Node k and o connect to n and j: p1 propagated (outside window)
  Node g connect to j, f and b: p2 propagated (outside window)
  Terminal p1 pulls k/o/g to top partition, and p2 pulls g to bottom

## Slide 7: Cut 4: Terminal Propagation
One terminal propagated
  Node n and j connect to o/k/g: p1 propagated
  Node i and j connect to e/f/a: no propagation (inside window)
  Terminal p1 pulls n and j to right partition

## Slide 8: Cut 5: Terminal Propagation
Three terminals propagated
  Node i propagated to p1, j to p2, and g to p3
  Terminal p1 pulls e and a to left partition
  Terminal p2 and p3 pull f/b/e to right partition

## Slide 9: Cut 6: Terminal Propagation
One terminal propagated
  Node n and j are propagated to p1
  Terminal p1 pulls o and k to left partition

## Slide 10: Cut 7: Terminal Propagation
Three terminals propagated
  Node j/f/b propagated to p1, o/k to p2, and h/p to p3
  Terminal p1 and p2 pull g and l to left partition
  Terminal p3 pull l and d to right partition

## Slide 11: Cut 8 to 15
16 partitions generated by 15 cuts
  HPBB wirelength = 23

## Slide 12: Comparison
Quadrature vs recursive bisection + terminal propagation
  Number of cuts: 6 vs 15
  Wirelength: 27 vs 23